## Slide 1: YARP and iCub code tutorials

## Slide 2: Software installation
www.yarp.it  Installation
http://wiki.icub.org/wiki/ICub_Software_Installation
Installation from sources
Linux virtual machine: http://www.icub.org/download/other/Ubuntu_1404_64-bit.zip

## Slide 3: Code available on github
https://github.com/iron76/Teaching
Type:
git clone git@github.com:iron76/Teaching.git

## Slide 4: Yarp from command line

## Slide 5: A (very) simple example: read data to/from a port
[on terminal 1] yarpserver
[on terminal 2] yarp read /read
[on terminal 3] yarp write /write /read
yarp write
/write
yarp read
/read
$ yarp write /write /read
Port /write listening at tcp://127.0.0.1:10012
yarp: Sending output from /write to /read using tcp
Added output connection from "/write" to "/read"
hello yarp
1 2 3
$ yarp read /read
Port /read listening at tcp://127.0.0.1:10002
yarp: Receiving input from /write to /read using tcp
hello yarp
1 2 3

## Slide 6: yarp name list yarp name query /read yarp name register PORT CARRIER IP NUMBER yarp name unregister PORT

## Slide 7: how the network grows
It is easy to add, for example, another reader…
Processes can run on different machines, with different OS
yarp write
/write
yarp read
/read
yarp read
/read2
yarp read
/read3
yarp connect /write /read
yarp connect /write /read2
…
yarp disconnect /write /read
yarp disconnect /write /read2

## Slide 8: yarpview
yarpdev --device test_grabber --name /cam/right
yarpdev --device test_grabber --name /cam/left
yarpview --name /view1
yarpview --name /view2
yarp connect /cam/right /view1
yarp connect /cam/left /view2

## Slide 9: YARP configuration file
Where is the yarp nameserver?
icub@ubuntu-1404-64-vm:~$ yarp detect
icub@ubuntu-1404-64-vm:~$ yarp conf
/home/icub/.config/yarp/yarp.conf
icub@ubuntu-1404-64-vm:~$ cat /home/icub/.config/yarp/yarp.conf
192.168.59.128 10000 yarp
yarpserver by default decides based on the available network card (i.e. eth0) on which adapter/ip to listen
You can manually modify the yarp.conf file to change adapter/ip.
yarpserver can accept that (--read) or overwrite it (--write).

## Slide 10: Connecting to mjpeg
yarpview –name /view
yarp connect /195.67.26.73:80 /view mjpeg+path./mjpg/video.mjpg
Alternatively you can register the remote address manually:
yarp name register /webcam mjpeg+path./mjpg/video.mjpg 195.67.26.73 80
And use /webcam as an alias
yarp connect /webcam /view
Make sure these CMake flags are enabled:
CREATE_OPTIONAL_CARRIERS=ON
ENABLE_yarpcar_mjpeg_carrier=ON
Run ccmake in YARP’s build directory

## Slide 11: Automation

## Slide 12: The YARP Manager
The yarpmanager is a graphic interface to monitor processes
It allows to start/stopping/monitor, redirect i/o
In addition it automates establishing connections between modules
…
…
.xml

## Slide 14: yarpmanager documentation
http://wiki.icub.org/yarpdoc/yarpmanager.html

## Slide 15
/node1
Starting a server
$node1: yarprun –server /node1
run a server, which will wait for commands on /node1
localhost
The manager has two ways to execute processes: locally (localhost) or through yarprun
yarprun is a server that waits for commands on a port
start/termination/kill monitor lifecycle
http://wiki.icub.org/yarpdoc/db/dd7/yarprun.html

## Slide 16
/pc1
/pc2
/pc3
/pc4
/pc104
tracker
yarpview –name /view1
iCubInterface
iKinCartesianSolver
iKinGazeCtrl

## Slide 17: Syntax
<application>
<name>Name of the application</name> //this can be anything, just a symbolic name
<dependencies>
<port>/port1 </port>
<port>/port2 </port>
</dependencies>
<module>
<name>mymodule1 </name>
<parameters>--threshold 1 --name /myName</parameters>
<node>localhost</node>
</module>
<module>
<name>mymodule2</name>
...
</module>
<connection>
<from>/port1</from>
<to>/otherport</to>
<protocol>udp</protocol>
</connection>
<connection>
…
</connection>
</application>

## Slide 18
<application>
<name>Name of the application</name> //this can be anything, just a symbolic name
<module>
<name>yarpdev</name>
<parameters>--device test_grabber --name /cam/right</parameters>
<node>localhost</node>
</module>
<module>
<name>yarpview</name>
<parameters>--name /view/right</parameters>
<node>localhost</node>
</module>
<connection>
<from>/cam/right</from>
<to>/view/right</to>
<protocol>udp</protocol>
</connection>
</application>
or any other node in the network:
/node1, /node2 etc..
E.g. on the iCub: icub14, icub15, icub-b11…

## Slide 19: Other tags
<dependencies>
<port>/icub/cam/left</port>
<port>/icub/cam/right</port>
</dependencies>
<module>
…
<workdir>C:/mydir</workdir>
<stdio>node3</stdio>
</module>

## Slide 20: CMake Basics

## Slide 21: Introduction
Open source build manager
Specify build parameters in a simple portable text format
Portable txt file
CMakeLists.txt
CMake
Project Files (i.e. Makefile or .sln)
Code, header files
Libraries
options
User interface
System ‘introspection’

## Slide 22: Problems solved by CMake
Write and maintain project files for multiple platforms
Optional components?
Build on more than a single machine: different OS have different libraries, same OS can be installed differently  automatically search for programs libraries header files
Build directory tree different from source tree
Handle dependencies
Static versus Dynamic libraries
…

## Slide 23: Basics
Commands (case insensitive)
Variables (case sensitive)
command(a b c)
set(FOO a b c)
command(${FOO})
command(“${FOO}”)
Consider:
set(PATH_TO_MY_FILE C:\program files\myfile)
command(${PATH_TO_MY_FILE})
command(“${PATH_TO_MY_FILE}”)

## Slide 24: Hello World with CMake
cmake_minimum_required(VERSION 2.8)
project(hello)
include_directories(${CMAKE_CURRENT_SOURCE_DIR})
message(STATUS "--> Hello from CMake")
if (WIN32)
message("--> Running on windows")
else()
message("--> Assuming running on Linux")
endif()
if (NOT EXISTS "${CMAKE_CURRENT_SOURCE_DIR}/hello.cpp")
message(FATAL_ERROR "File hello.cpp not found!")
endif()
add_executable(hello hello.cpp)

## Slide 25: How to run CMake
Source versus build directories
From command line:
  mkdir build
  cd build
  cmake ../ or ccmake ../
From gui:
  mkdir build
  cmake-gui
  Set source and build directories
Hit “c” until you get “g”
When build = source dir: in source build
When build != source dir: out of source build

## Slide 26: Cache
Some variables are determined only once and cached on disk; CMake will not touch them, only the user can
E.g. user options or result of system introspection, info that are expensive to determine (compiler to use, system libraries, etc..)
To do a fresh restart, clean the cache
  From the gui
  Remove CMakeCache.txt

## Slide 27: Commands on targets
add_executable(name file1.cpp file2.cpp header1.h header2.h)
target_link_libraries(name libname)
add_library(name file1.cpp file2.cpp header1.h)
include_directories(dir1 dir2)
add_definitions(-DFOO -DBAR)

## Slide 28: Example:
#if _ENABLE_DEBUG_
printf(“Value of variable v is %d”, v);
#endif
option(ENABLE_DEBUG "Enable debugging messages"
FALSE)
if (ENABLE_DEBUG)
message(STATUS "Debugging messages are enabled")
add_definitions(-D_ENABLE_DEBUG_)
endif()

## Slide 29: Installation
In some builds include an installation step
You can add installation rules using CMake
install(TARGETS myExe RUNTIME DESTINATION <dir>)
install(FILES files DESTINATION <dir>)
<dir> can be:
Absolute path
Relative path, in this case it will be CMAKE_INSTALL_PREFIX\<dir>
The user can customize CMAKE_INSTALL_PREFIX

## Slide 30: Hello World with CMake (2)
...
add_executable(hello hello.cpp)
install(TARGETS hello
RUNTIME DESTINATION ${CMAKE_CURRENT_SOURCE_DIR}/../bin)

## Slide 31: Finding libraries
The problem
You want to compile an executable that links libraries from another package, e.g. YARP
Naïve way:
cmake_minimum_required(VERSION 2.8)
project(hello)
include_directories(“C:\Program files\yarp\include”)
add_executable(hello hello.cpp)
target_link_libraries(hello “C:\Program files\yarp\lib\libYARP_OS.lib”)

## Slide 32: Finding libraries
The problem
You want to compile an executable that links libraries from another package, e.g. YARP
Naïve way:
cmake_minimum_required(VERSION 2.8)
project(hello)
include_directories(“C:\Program files\yarp\include”)
add_executable(hello hello.cpp)
target_link_libraries(hello “C:\Program files\yarp\lib\libYARP_OS.lib”)
Installation dependent
Os dependent (.a in Linux)

## Slide 33: Finding libraries…
CMake has a few commands that can be used to find directories, executables and libraries inside a computer
find_file(<var> name dir1 dir2)
find_library(<var> name dir1 dir2)
find_path(<var> name dir1 dir2)
However there is a better interface…

## Slide 34: find_package()
A package should provide you:
  Paths to libraries
  Paths to header files
  Linker flags (if any)
find_package(<PACKAGE> [VERSION])
This function attempts to locate the package called <PACKAGE> and will return a set of variables:
<PACKAGE>_FOUND
<PACKAGE>_INCLUDE_DIRS
<PACKAGE>_LIBRARIES
<PACKAGE>_VERSION
<PACKAGE>_VERSION_MAJOR
<PACKAGE>_VERSION_MINOR

## Slide 35: Example:
find_package(YARP)
YARP_FOUND
YARP_INCLUDE_DIRS
YARP_LIBRARIES

## Slide 36
How does find_package() work?
  Looks for system directories
  C:\Program files\<package>
  /usr/<package>
  /usr/local/<package>
  …
  Look for environment variables, very popular <PACKAGE>_DIR
CMake does not enforce a particular set of variables each package set different variables
Other examples:
<PACKAGE>_INCLUDE_DIR
<PACKAGE>_LIBS
etc..

## Slide 37: Hello YARP
cmake_minimum_required(VERSION 2.8)
project(myproject)
find_package(YARP)
include_directories(${YARP_INCLUDE_DIRS})
add_executable(hello hello.cpp)
target_link_libraries(hello ${YARP_LIBRARIES})
add_executable(hello2 hello.cpp)
target_link_libraries(hello2 ${YARP_LIBRARIES})

## Slide 38
#include <stdio.h>
#include <yarp/os/Time.h>
int main()
{
printf("Starting the application\n");
int times=10;
while(times--)
{
printf("Hello iCub\n");
yarp::os::Time::delay(0.5); //wait 0.5 seconds
}
printf("Goodbye!\n");
}
Hello yarp

## Slide 39: Ports

## Slide 40: A (very) simple example: read data to/from a port
[on terminal 1] yarpserver
[on terminal 2] yarp read /read
[on terminal 3] yarp write /write /read
yarp write
/write
yarp read
/read
$ yarp write /write /read
Port /write listening at tcp://127.0.0.1:10012
yarp: Sending output from /write to /read using tcp
Added output connection from "/write" to "/read"
hello yarp
1 2 3
$ yarp read /read
Port /read listening at tcp://127.0.0.1:10002
yarp: Receiving input from /write to /read using tcp
hello yarp
1 2 3

## Slide 41: How do we get this?
int main(int argc, char *argv) {
Network yarp;
Port inPort;
inPort.open("/relay/in");
Port outPort;
outPort.open("/relay/out");
while (true) {
cout << "waiting for input" << endl;
Bottle input,output;
inPort.read(input);
output=input;
cout << "writing " << output.toString().c_str() << endl;
outPort.write(output);
}
return 0;
}
relay
/relay/in
/relay/out
Let’s now to write a simple “relay” executable which takes whatever comes from a port and forwards it to another one.

## Slide 42: Connect the new module to our network
relay
/relay/in
/relay/out
yarp write
/write
yarp read
/read
yarp disconnect /write /read
yarp connect /write /relay/in
yarp connect /relay/out /read

## Slide 43: how the network grows
relay
/relay/in
/relay/out
It is easy to add, for example, another reader…
Processes can run on different machines, with different OS
yarp write
/write
yarp read
/read
yarp read
/read2
yarp read
/read3
yarp connect /relay/out /read
yarp connect /relay/out /read2
…

## Slide 44: BufferedPort
In the previous example timing between ports is coupled:
  The reader waits until data arrives to the port
  The writer waits until data is transmitted
Buffered ports allow decoupling time:
  non blocking read
  non blocking write
May loose messages

## Slide 45
Read:
BufferedPort<Bottle> p; // Create a port.
p.open("/in"); // Give it a name on the network.
while (true) {
Bottle *b = p.read(); // Read/wait for until data arrives. ...
// Do something with data in *b
}
Write:
BufferedPort<Bottle> p; // Create a port.
p.open("/out"); // Give it a name on the network.
while (true) {
Bottle& b = p.prepare(); // Get a place to store things. ...
// Generate data.
p.write(); // Send the data.
}

## Slide 46
C1
C2
Msg
Msg
Msg
BufferedPort
C1
Client1
Client2
Msg
Msg
Msg
Msg m =port.prepare();
//fill m
Port.write()
Msg *m=port.read();
//read from m
Delay(100000)

## Slide 47
BufferedPort<Bottle> p;
...
Bottle *b = p.read(false);
if (b!=NULL) {
// data received in *b
}
Polling: when you do not want to wait for input data:

## Slide 48
Getting callbacks

## Slide 49
class DataPort : public BufferedPort<Bottle> {
virtual void onRead(Bottle& b) {
// process data in b
}
};
...
DataPort p;
p.useCallback(); // input should go to onRead() callback
p.open("/in");
Callbacks: useful if you want to be notified when data arrives
Easy to do with BufferedPorts

## Slide 50
class DataProcessor : public PortReader {
virtual bool read(ConnectionReader& connection) {
Bottle b;
bool ok = b.read(connection);
if (!ok) return false;
// process data in b
return true;
}
};
Port p;
p.open(..)
DataProcessor processor;
...
p.setReader(processor); // no need to call p.read() on port any more.
Things are a bit more complicated with normal ports

## Slide 51: Replies in a callback
class DataProcessor : public PortReader {
virtual bool read(ConnectionReader& connection) {
Bottle in, out;
bool ok = in.read(connection);
if (!ok) return false;
... // process data "in", prepare "out"
ConnectionWriter *returnToSender = connection.getWriter();
if (returnToSender!=NULL) {
out.write(*returnToSender);
}
return true;
}
};
DataProcessor processor;
...
p.setReader(processor); // no need to call p.read() on port any more.

## Slide 52
Bidirectional communication:
Getting replies

## Slide 53: Client side
RpcClient p; // Create a port.
p.open("/out"); // Give it a name on the network.
while (true) {
Bottle in,out; // Make places to store things.
... // prepare command "out".
p.write(out,in); // send command, wait for reply.
... // process response "in".
}

## Slide 54: Server side
RpcServer p; // Create a port.
p.open("/in"); // Give it a name on the network.
Bottle in, out; // Make places to store things.
while (true) {
p.read(in,true); // Read and warn that we'll be replying.
... // Do something with data, prepare reply
p.reply(out); // send reply.
}

## Slide 55: YARP modules: RFModule

## Slide 56: The RFModule class
You create a new module by deriving a new class from RFModule
class MyModule:public RFModule
{
public:
bool configure(ResourceFinder &rf)
{ //module configuration }
bool close()
{ //code executed at shutdown }
};
MyModule module;
ResourceFinder rf;
//configure resource finder
module.runModule(rf); //if configure returns true block here until the module closes
get parameters form RF and configure the module, return true on success, false otherwise
perform cleanup, close ports, delete memory
We skip this

## Slide 57
What does a module do?
Nothing, really…

## Slide 58
What does a module do?
Nothing, really…
Wait for termination signal (message or ctrl-c)
Can be configured to receive messages from a port/keyboard
Can perform periodic activities
It is a container for active objects (threads)

## Slide 59: Attach callbacks
class MyModule::RFModule
{
Port handlerPort;
…
bool configure(ResourceFinder &rf)
{
// use rf to configure your module
handlerPort.open(“/myModule”);
attach(handlerPort);
…
}
…
}

## Slide 60
Now add a respond message to catch data from terminal or/and the handler port
// Message handler. Just echo all received messages.
bool respond(const Bottle& command, Bottle& reply)
{
cout<<"Got something, echo is on"<<endl;
if (command.get(0).asString()=="quit")
return false;
else
reply=command;
return true;
}

## Slide 61: Periodic Activities
In MyModule overload:
double getPeriod()
{ return 1; }
bool updateModule()
{
// place here code that will be
// executed every “getPeriod” seconds
return true;
}
define period in seconds
this function will be executed until termination

## Slide 62
You can interrupt blocking reads on ports in the interrupt method:
bool interruptModule()
{
port1.interrupt();
port2.interrupt();
…
return true;
}

## Slide 63
Threads

## Slide 64
#include <yarp/os/Thread.h>
Class yarp::os::Thread
{
public:
virtual bool start();
virtual bool stop();
virtual bool threadInit();
virtual bool threadRelease();
virtual void run();
bool isStopping();
};
yarp::os::Thread is the class that provides thread support in YARP

## Slide 65
#include <yarp/os/Thread.h>
Class MyThread: public Thread
{
public
void run()
{
while(!isStopping)
//thread body
}
};
MyThread thread;
thread.start();
…
thread.stop();
You can implement your own thread by deriving a class from Thread

## Slide 66
Override threadInit() and threadRelease() to peform initialization and cleanup:
Class MyThread: public Thread
{
public
bool threadInit()
{
//perform init tasks, memory allocation…
//return true if successful false otherwise
}
bool threadRelease()
{
//cleanup memory, release resources…
}
void run() {..}
}

## Slide 67
#include <yarp/os/RateThread.h>
Class yarp::os::RateThread
{
public:
RateThread(int period); //periodicity, ms
virtual bool start();
virtual bool stop();
virtual bool threadInit();
virtual bool threadRelease();
virtual void run();
};
Very often you want a thread to perform periodic activities (e.g. control loop)
RateThread supports periodic threads

## Slide 68
#include <yarp/os/RateThread.h>
Class MyRateThread: public RateThread
{
public:
MyRateThread(int p=50): RateThread(p){}
void run()
{
…
}
};
MyRateThread rthread;
rthread.start();
…
rthread.stop();

## Slide 69
Getting images

## Slide 70
YARP defines an image class
ImageOf<…> is a template class that provides:
  basic methods for image manipulation
  support for remotization (i.e. images can travel across Ports/the network)
data format is opencv compatible
  See: YARP image class online documentation

## Slide 71
Images from cameras are streamed from two ports:
  /icub/cam/right
  /icub/cam/left
Easily read:
  BufferedPort<ImageOf<PixelRgb> > imagePort;
  imagePort.open("/imageProc/image/in");
  ImageOf<PixelRgb> *image = imagePort.read(); //read an image:

## Slide 72
BufferedPort<ImageOf<PixelRgb> > imagePort;
imagePort.open("/imageProc/image/in");
//read an image:
ImageOf<PixelRgb> *image = imagePort.read();
//do something with the image, for example cycle through all pixels
int ct=0
for (int x=0; x<image->width(); x++) {
for (int y=0; y<image->height(); y++) {
PixelRgb& pixel = image->pixel(x,y);
// very simple test for blueishness
// make sure blue level exceeds red and green by a certain factor
if (pixel.b>pixel.r*1.2+10 && pixel.b>pixel.g*1.2+10) {
xMean += x;
yMean += y;
ct++;
}
}
}
if (ct>0) {
xMean /= ct;
yMean /= ct;
}
printf("Best guess at blue target: %g %g\n", xMean, yMean);

## Slide 73
  Complete tutorial shows a program example that control the gaze of the robot to fixate a blue ball:
  http://wiki.icub.org/iCub/dox/html/icub_basic_image_processing.html

## Slide 74: Controlling the simulator
Set of ports for parts {head} {left_arm} {torso} etc…
Ports:
/icubSim/head/rpc:i
/icubSim/head/command:i
/iicubSim/head/state:o
icub@ubuntu-1404-64-vm:~$ yarp rpc /icubSim/head/rpc:i
>>get encs
Response: [is] encs (-0.000015 0.000004 -0.000004 -0.0 0.0 -0.0) [tsta] 1 1434026836.655992 [ok]
>>set pos 0 -10
Response: [ok]
>>set pos 1 20
Response: [ok]
>>set poss (0 0 0 0 0 0)
Response: [ok]
>>get encs
Response: [is] encs (-0.0005 0.000971 -0.000004 -0.0 0.0 -0.0) [tsta] 2 1434026858.553787 [ok]
>>

## Slide 75
set pos 0 10
set vel 1 5
get enc 0
enc is 5
ack
remote_controlboard
server_controlboard
Simulator/iCub
/client/left_arm/rpc:i
/client/left_arm/state:i
/client/left_arm/command:o
/iCubSim/left_arm/rpc:i
/iCubSim/left_arm/state:i
/iCubSim/left_arm/command:o
IPositionControl
IVelocityControl
IEncoders
User code
positionMove()
getEncoders()
…

## Slide 76
http://wiki.icub.org/yarpdoc/classyarp_1_1dev_1_1IPositionControl.html
http://wiki.icub.org/yarpdoc/classyarp_1_1dev_1_1IVelocityControl.html

## Slide 77: PolyDriver
PolyDriver
DeviceDriver
open(params)
close()
view(interface1)
view(interface2)
open()
close()
Use interface1
Use interface2
User Code

## Slide 78
/icubSim/cam/right
/viewer/cam/left
/viewer/cam/right
/detector/image/out
/detector/target
/detector/image/in
/viewer/object
/icubSim/cam/left
simulator
object_detector
yarpview
yarpview
yarpview

## Slide 79
/tracker/target:i
Back to simulator
… head/rpc:I
… head/…
/icubSim/cam/right
/viewer/cam/left
/viewer/cam/right
/detector/image/out
/detector/target
/detector/image/in
/viewer/object
/icubSim/cam/left
simulator
lookAtLocation
object_detector
yarpview
yarpview
yarpview