## Slide 1
iCub Facility
Istituto Italiano di Tecnologia, Genova
Robot programming
Lorenzo Natale, Ali Paikan, Alessandro Roncone, Ugo Pattacini, Daniele Domenichelli
Genova, July 2015

## Slide 2: Program
2nd July, 2015 – h 10:12 – Sala Natta - Lesson 1: Introduction to the middleware
3nd July, 2015 – h 10:12 – Sala Volta - Lesson 2: Hello world, command line tools. YARP threads and YARP modules
6nd July, 2015 – h 10:12 – Sala Natta - Lesson 3: YARP Manager, port monitor, and realtime computing with YARP
7nd July, 2015 – h 14:16 – Sala Dulbecco - Lesson 4: Image processing and Computer Vision
8nd July, 2015 – h 14:16 – Sala Dulbecco - Lesson 5: The Gaze controller and the Cartesian Controller for efficient inverse kinematics
10nd July, 2015 – h 14:16 – Sala Dulbecco - Lesson 6: Software development with GIT, the GIT workflow

## Slide 3: References
YARP: www.yarp.it
  Documentation
  Papers (see also references in this presentation)
iCub: http://wiki.icub.org/wiki/Manual
CMake:
  www.cmake.org  documentation & wiki
  Mastering CMake, by Kitware Inc.
C++:
  Thinking in C++, Bruce Eckel
  The C++ programming language, Bijarne Stroustrup
  Anything else

## Slide 4: Motivations

## Slide 5: Complex behaviors

## Slide 6: Integration of software components

## Slide 7: Complex behaviors

## Slide 8: Key issues
  Asynchronous development
  Variability: various scenarios and platforms
  Lack of standards
  Inherent complexity, distributed processing, lots of sensors, real-time
  Fluctuation in hardware and algorithms, lots of open questions

## Slide 9: Software architecture
Major cost in software development is debugging, recycling code is key
Divide and conquer
Modularity
Factor out platform specificities
  Hardware Abstraction Layer
  Communication Abstraction
  Operating system
  Parameters
  Computing infrastructure

## Slide 10: Separation of concerns (5C)
Goal: separate software components
Computation
Communication
Configuration
Coordination
Composition
BRICS Component Model, 2013
What we are interested in
Dependent on the hardware, network topology
Application dependent

## Slide 11
output myAlgorithm(input)
{
...
out = call alg1(in)
…
out = call alg2(in)
getImage() // from usb camera
…
}
output alg1(input)
{code}
output alg2(input)
{code}
Component driven software development

## Slide 12
Program2
output myAlgorithm(input)
{
...
out = call alg1(in)
…
out = call alg2(in)
getImage() // from usb camera
…
}
output alg1(input)
{code}
output alg2(input)
{code}
myAlg()
alg1()
Program1
Component driven software development
middleware
Program2
alg2()
middleware
middleware
hardware

## Slide 13
Program2
output myAlgorithm(input)
{
...
out = call alg1(in)
…
out = call alg2(in)
getImage() // from usb camera
…
}
output alg1(input)
{code}
output alg2(input)
{code}
myAlg()
alg1()
Program1
Component driven software development
middleware
Program2
alg2()
middleware
middleware
hardware

## Slide 14: Components: some examples from the iCub repository
Algorithms for motion computation and egomotion compensation
Machine learning for vision
Disparity map
Action recognition
Segmentation
See https://github.com/robotology

## Slide 15: Component driven development
Modular software: simple structure, data encapsulation, interface
Reconfigurable components
Reduced coupling: interaction between components happens through pre-defined standards (no direct inclusion of header files)

## Slide 16: Communication paradigm
Publish/Subscribe
  Space, time, synchronization decoupling
Remote Procedure Calls (RPC)
  Remote invocation of object
  Synchronous nature (although variant exists)

## Slide 17: Publish/Subscribe
Space decoupling: the interaction parties do not need to know each other; publisher publish events through an event service and the subscribers get these events indirectly through the event service
Time decoupling: interaction parties do not need to be actively participating in the interaction at the same time, publisher might publish events while subscribers is disconnected and subscribers might get notified of an event while the original publisher is disconnected
Synchronization decoupling: publishers are not blocked while producing events and subscribers can get asynchronously notified (through callback) of the occurrence of the event while performing concurrent activity
Eugster, et al., The Many Faces of Publish/Subscribe, 2003.

## Slide 18: YARP approach
Limited form of publish-subscribe
Observer patter: subscribers register their interest directly with publishers, which mange subscriptions and sends events
Publishers notify subscribers synchronously or asynchronously
Space decoupling (from user perspective)
Time coupling
Dynamic (re)configuration
See also:
YARP: Yet Another Robot Platform, G. Metta, P. Fitzpatrick, L. Natale, 2006
Stewart et al., Design of Dynamically Reconfigurable Real-time Software Using Port-Based Objects, 1997

## Slide 19: iCub software architecture
ROBOT
…
/arm/encs
/arm/trqs
/hand/touch
/arm/cmd
/camera

## Slide 20: iCub software architecture
...
ROBOT
…
/arm/encs
/arm/trqs
/hand/touch
/arm/cmd
/camera
Reaching
...
...
...
Grasping
Object det.
...
...
...
...
...
...

## Slide 21: iCub software architecture
...
ROBOT
…
/arm/encs
/arm/trqs
/hand/touch
/arm/cmd
/camera
Reaching
...
...
...
Grasping
Object det.
...
...
...
...
...
...

## Slide 22: iCub software architecture
...
ROBOT
…
/arm/encs
/arm/trqs
/hand/touch
/arm/cmd
/camera
Reaching
...
...
...
Grasping
Object det.
...
...
...
...
...
...

## Slide 23: iCub software architecture
...
ROBOT
…
/arm/encs
/arm/trqs
/hand/touch
/arm/cmd
/camera
Reaching
...
...
...
Grasping
Object det..
...
...
...
...
...
...

## Slide 24: iCub software architecture
...
ROBOT
…
/arm/encs
/arm/trqs
/hand/touch
/arm/cmd
/camera
Reaching
...
...
...
Grasping
Object det..
...
...
...
...
...
...
Viewer
...

## Slide 25: iCub software architecture
...
ROBOT
…
/arm/encs
/arm/trqs
/hand/touch
/arm/cmd
/camera
Reaching
...
...
...
Grasping
Object det..
...
...
...
...
...
...
Viewer
...

## Slide 26: iCub software architecture
...
ROBOT
…
/arm/encs
/arm/trqs
/hand/touch
/arm/cmd
/camera
Reaching
...
...
...
Grasping
Object det..
...
...
...
...
...
...
Viewer
...
mcast
mcast
udp
udp
udp
udp
udp
udp

## Slide 27: iCub software architecture
...
ROBOT
…
/arm/encs
/arm/trqs
/hand/touch
/arm/cmd
/camera
Reaching
...
...
...
Grasping
Object det..
...
...
...
...
...
...
Viewer
...
mcast
mcast
udp
udp
udp
udp
udp
udp

## Slide 28: YARP: main features
Peer-to-peer, loosely coupled, communication
Very stable code base >10 years old
Flexibility and minimal dependencies, fits well with other systems
  Easy install with binaries on many OSes/distributions (Ubuntu, Debian, Windows, MacOs
  Recently added: channel prioritization with QoS and thread priorities
  Many protocols:
  Built-in: tcp/udp/mcast
  Plug-ins: ROS tcp, xml rpc, mjpg etc..

## Slide 29: Interfaces
Define interfaces to motors and sensors so to minimize the impact of changes in the hardware
Also: network allow remotization

## Slide 30: Interfaces
…
…
read encoders
read IMU
read FT
…
get image
...
set position
.
External loops
Robot Interface
…
…
read encoders
read IMU
read FT
…
get image
...
set position
Loops on board
Network
Network Stub
Network Stub
Robot Interface
Robot

## Slide 31: Interfaces
…
…
read encoders
read IMU
read FT
…
get image
...
set position
Control loops
Walkman
Robot Interface
Gazebo
COMAN
iCub
  Recycle code across different robots and simulators (testing/fast prototyping)

## Slide 32: YARP plugins
YARP includes a plugin system for drivers and protocols (carriers)
Interchangeable carriers allow:
  interfacing existing software with ports (without bridges)
  change significantly port behavior
Examples:
  ROS, mjpeg, xml rpc, etc…
  bayer carrier, priority based communication

## Slide 33: Examples
Bayer Camera
/camera
receiver
YARP
yarp connect /camera /receiver rec.bayer

## Slide 34: Examples
Bayer Camera
/camera
receiver
YARP
receiver
YARP
yarp connect /camera /receiver rec.bayer
yarp connect /65.52.88.202:5159 /receiver mjpeg
MJPG camera
http://65.52.88.202:5159

## Slide 35: Examples
Bayer Camera
/camera
receiver
YARP
receiver
YARP
yarp connect /camera /receiver rec.bayer
yarp connect /65.52.88.202:5159 /receiver mjpeg
receiver
YARP
Camera.msg
yarp connect /image@/camera /receiver
MJPG camera
http://65.52.88.202:5159
ROS
Node: /camera
Topic: /image

## Slide 36: Success story
Whole-Body Modules
RobotInterface
Locomotion
Module
Manipulation
Modules
Perception
Pilot
Interface
Footstep &
Trajectory Planners
Coman
Walkman

## Slide 37: Simulators & robots
iCub, COMAN, Walk-man, ARMAR III
iCub_SIM (in the iCub main repository)
Gazebo (https://github.com/robotology/gazebo-yarp-plugins)
Robotran
Robotran-Yarp interface: a framework for real-time controller development based on multibody dynamics simulation, T. Habra, et al., 2015
Paikan et al., Transferring Object Grasping Skills and Knowledge Across Different Robotic Platforms, ICAR 2015

## Slide 38: Managing complexity
In a modular system integration becomes an issue:
Execution and monitoring
Development
Coordination

## Slide 39: Execution and monitoring: YARP manager
Available resources
Required
modules connections
nodes
resources

## Slide 40: Tools for rapid development
YARP builder: graphical tool to design application
Interface Definition Language (IDL):
  formalization of types and interfaces between modules
  automatic generation of message handlers

## Slide 41: Coordinating modules

## Slide 42: Arbitration and coordination
Paikan, A., et. al., Data Flow Port's Monitoring and Arbitration, Joser 2014.

## Slide 43
Arbitration and coordination

## Slide 44: Our solution: Port Monitor

## Slide 45: Our solution: Port Monitor
if (C1.certainty > 0.9)
accept(C1)
else
accept(C2)
if (check(C1)
dispatch(event)
C1=filter(C1)
dispatch(C1)
If (C1)
T1=getTime()
arbitration
coordination
filtering
logging
Monitoring delays, QoS

## Slide 46
Paikan, A., et al., Enhancing software module reusability using port plug-ins: an experiment with the iCub robot, IROS 2014.

## Slide 47: Improving determinism

## Slide 48: Threads and scheduling, quick overview
Issues:
Scheduling and interrupt latency
Certain operations may be blocking i.e. not preemtable (usually system calls)
System calls: file management, process management, I/O, memory requests, communication (shared memory), error handling

## Slide 49: Which RT solution
Standard Linux
Linux with RT patch
Xenomai/RTAI

## Slide 50: The latency of a Linux thread with the highest priority (period 1ms)
Thread latency in Linux-pae-3.2.0 (SCHED_FIFO)
(period: 1ms, PC104 / 1Ghz )
Notes: During the experiment, system was overloaded by:
4 processes, each calculates the square root of a random number
4 processes, each flushes data buffered in memory to disk (sync()).
4 processes to contentiously allocate and release memory
4 process writing to hard drive (write())
Thread scheduled with 1khz
PC104, Dual Core 1.0GHz
Linux Debian Wheezy (7.0)
Different kernel:
Kernel pae-3.2.0
Kernel preemption-3.2.0
Kernel Xenomai-3.5.7

## Slide 51: The latency of a Linux thread with preemption patch (period: 1ms, PC104 / 1Ghz )
Thread latency in Linux-rt-3.2.0

## Slide 52: The latency of a Linux thread with Xenomai patch (period: 1ms, PC104 / 1Ghz )
Thread latency in Linux-xenomai-3.5.7

## Slide 53
HOST1
Robot
With priority
Standard YARP

## Slide 54: System under heavy load

## Slide 55: After adjusting thread priorities

## Slide 56
HOST1
Robot
switch
With priority
Standard YARP

## Slide 57
HOST1
Robot
switch
20%/70% load

## Slide 58
HOST1
Robot
switch
HOST2
20%/70% load

## Slide 59: References
Ali Paikan, Silvio Traversaro, Francesco Nori and Lorenzo Natale, "A Generic Testing Framework for Test Driven Development of Robotic Systems", In Lecture Notes in Computer Science (MESAS15), Springer, pp. , 2015
Paikan, A., Domenichelli, D., and Natale, L., Communication channel prioritization in a publish-subscribe architecture, in Proc. Software Engineering and Architectures for Realtime Interactive Systems Workshop, Arles, France, 2015.
Paikan, A., Tikhanoff, V., Metta, G., and Natale, L., Enhancing software module reusability using port plug-ins: an experiment with the iCub robot, in Proc. IEEE/RSJ International Conference on Intelligent Robots and Systems, Chicago, Illinois, 2014.
Fitzpatrick, P., Ceseracciu, E., Domenichelli, D., Paikan, A., Metta, G., and Natale, L., A middle way for robotics middleware, Journal of Software Engineering for Robotics, vol. 5, no. 2, pp. 42-49, 2014.
Paikan, A., Fitzpatrick, P., Metta, G., and Natale, L., Data Flow Port's Monitoring and Arbitration, Journal of Software Engineering for Robotics, vol. 5, no. 1, pp. 80-88, 2014
Metta, G., Fitzpatrick, P., Natale, L., YARP: Yet Another Robot Platform, International Journal of Advanced Robotics Systems, special issue on Software Development and Integration in Robotics, Volume 3, Issue 1, pp. 43-48, March 2006
Patrick Th. Eugster, Pascal A. Felber, Rachid Guerraoui, and Anne-Marie Kermarrec. 2003. The many faces of publish/subscribe. ACM Comput. Surv. 35, 2 (June 2003), 114-131.
David, B. Stewart, Richard, A. Volpe, Pradeep, K. Khosla, Design of Dynamically Reconfigurable Real-Time Software Using Port-Based Objects, IEEE Trans. On Software Engineering, 23(12), 1997
Dušan Bálek, František Plášil, Software Connectors and Their Role in Component Deployment, New Developments in Distributed Applications and Interoperable Systems, 70, 2002, pp. 69-84.
Farhad Arbab: Reo: a channel-based coordination model for component composition. Mathematical Structures in Computer Science 14(3):329--366, 2004.